## Slide 1: A PROJECT REPORT ON
"TRANSFORMER OIL RECLAMATION"
MANSAPURAM PETROCHEM PVT. LTD. |  | 
 | MANDIDEEP, MADHYA PRADESH | 
GUIDED BY:
MR. SPARSH SINGH
SENIOR MANAGER
MANSAPURAN PETROCHEM.
SUBMIT T ED BY:
R OSHAN BHUJANG
DEPAR T MENT OF PET R O - CHEMICAL ENGINEER ING
UNIV ER SITY INST ITUT E OF T ECHNOLOGY, R GPV, BHOPAL ( M. P)

## Slide 2: CERTIFICATE
This is to Certify that Mr. Roshan Bhujang Pursuing Bachelor of Technology in Petro-chemical Engineering from Department of Petro-Chemical Technology, University Institute of Technology, RGPV, Bhopal (M.P) has successfully completed a training Report on “TRANSFORMER OIL RECLAMATION” at MANSAPURAM
PETROCHEM PVT. LTD. from 31th of October 2022 to 30th of November 2022 and has submitted a copy of training report after successful completion of training at MANSAPURAM PETROCHEM PVT. LTD We found him as a hardworking, sincere and diligent person and his behavior and conduct was good.
Date: / /
Mr. Sparsh Singh
“TRANSFORMER OIL RECLAMATION”

## Slide 3: ACKNOWLEDGEMENT
It is my pleasure to be indebted to various people who directly or indirectly contributed in
the development of the work and who influenced my thinking and acts during the course of study.
I wish to thank MANSAPURAM PETRO-CHEM PVT. LTD. for conducting the training program.I am so thankful to the every team member of MANSAPURAM PETROCHEM PVT. LTD. as they help a lot me to gain knowledge during my course.
I would like to thank Mr. Sparsh Singh, S.M. (Mansapuram Petrochem Pvt. Ltd.), who provided me continuous guidance and his valuable time in accomplishing my Project Report
Lastly, I would like to thank the almighty, my parents and my professors at UIT, RGPV, Bhopal for their moral support and my friends with whom I shared my day-to-day experience and received lots of suggestions that improved my quality of work.
Name: Roshan Bhujang
“TRANSFORMER OIL RECLAMATION”

## Slide 4: CONTENTS
“TRANSFORMER OIL RECLAMATION”
Sr. No. | Topic | Page No.
1. | Introduction to MANSAPURAM PETRO- CHEM. | 1
2. | Transformer Oil. | 2
3. | Types of Transformer Oil. | 3
4. | Properties of Transformer Oil. | 4
5. | List of Plant and Machinery. | 5 - 7
6. | Process of Reclamation of Transformer Oil. | 8 - 10
7. | Process Flow Chart of Plant. | 11
8. | Parameters of Transformer Oil. | 13
9. | Conclusion. | 14
10. | References. | 15

## Slide 5: INTRODUCTION TO MANSAPURAM PETROCHEM PVT. LTD.
“TRANSFORMER OIL RECLAMATION”
1
Mansapuram Petrochem Transformer oil Recycler and hazardous waste Disposal is an MSME Level private-based company certified by Madhya Pradesh Pollution Control Board established in 1995, at Plot No 205-A New, Industrial Area, Mandideep, Madhya Pradesh 462046. Its main role is to recycle or Reclaiming the transformer oil and make it reusable for transformers.
This plant is capable of purifying 147,000 liters of transformer oil in 24 hours with following the proper guidelines of the pollution control board.

## Slide 6: TRANSFORMER OIL
Insulating oil in an electrical power transformer is commonly known as transformer oil. It is normally obtained by fractional distillation and subsequent treatment of crude petroleum. That is why this oil is also known as mineral insulating oil.
Transformer oil is highly refined mineral oil that is stable at high temperatures and has excellent electrical insulating properties.
Transformer oil serves mainly two purposes, one it is liquid insulation
in electrical power transformer and the other is it dissipates heat of the transformer i.e. it acts as a coolant. In addition to these, this oil serves other two purposes, it helps to preserve the core and winding as these are fully immersed inside oil and another important purpose of this oil is, it prevents direct contact of atmospheric oxygen with cellulose made paper insulation of windings, which is susceptible to oxidation.
“TRANSFORMER OIL RECLAMATION”
2

## Slide 7: TYPES OF TRANSFORMER OIL
3
There are different type of transformer oil generally,
Paraffin-based oil.
Silicon-based oil.
Naphtha-based oil
are used as transformer oil.
“TRANSFORMER OIL RECLAMATION”

## Slide 8: PROPERTIES OF TRANSFORMER OIL
4
“TRANSFORMER OIL RECLAMATION”
Basically every materials have two properties, chemical property and physical property. There are two types of properties of transformer insulating oil and they are:
Chemical properties of transformer oil :-
Neutralization value
Oxidation Stability
Physical properties of transformer oil:
Moisture Content
Interfacial tension
Flash point
Viscosity
Pour point

## Slide 9: LIST OF PLANT AND MACHINERY
5
"TRANSFORMER OIL RECLAMATION"
Sr. No. | Machine / Instrument Name
1. | M.S. DISTILLATION VESSEL – 1 NO.
2. | M.S. CONDENER FLOATING HEAD – 1 NO.
3. | M.S. AFTER COOLER – 1 NO.
4. | COOLING PACKIN RINGS
5. | INDUCED DRAFT FRP COOLING TOWER – 1 NO.
6. | PRODUCT RECEIVER – 3 NO.
7. | THERMICFLUID BOILER – 1 NO.

## Slide 10
Sr. No. | Machine / Instrument Name
8. | COOLING WATER AND CIRCULATION PUMP – 1 NO.
9. | OIL TRANSFER PUMP – 1 NO.
10. | LEVAL PRESSURE AND TEMPERATURE INDICATORS
11. | STRUCTURE AND PLATFORMS
12. | PIPE LINES AND VALVES
13. | ELECTRICAL INSTALLATION
14. | INSULATION OF EQUIPMENTS AND PIPELINES
6
"TRANSFORMER OIL RECLAMATION"

## Slide 11
Sr. No. | Machine / Instrument Name
15. | EFFULENT TREATMENT PLANT
16. | DEHYDRATION TANK
17. | CLAY TREATMENT TANK
18. | FILTER PRESS
19. | SETTING TANK
20. | THERMIC FLUID
7
"TRAMSFORMER OIL RECLAMATION'

## Slide 12: PROCESS OF RECLAMATION OF TRANSFORMER OIL
8
"TRAMSFORMER OIL RECLAMATION'
There are main 4 storage tanks in the plant, each tank can store 14000 liters of transformer oil, 2 tanks for burned transformer oil, and another 2 tanks for purified transformer oil. Firstly burned transformer oil is loaded into the storage tanks of the plant. Now the reclamation process of transformer oil is started from here, 7000 liters of burned transformer oil from the storage tank is transferred to the heating tank through pumps and pipelines. Now oil is heated with thermic fluid with the help of a boiler up to 160 °C which separates moisture and gases. Heating the oil will make it easier to filter because of the decrease in oil viscosity.

## Slide 13
After the oil reaches its required temperature then clay is added to the heating tank for the clay treatment, by clay treatment process moisture content will absorbs by the clay and remove unwanted gases from the transformer oil and enhance the physical and electrical properties of the oil.
9
"TRAMSFORMER OIL RECLAMATION'

## Slide 14
After the clay treatment, the oil is passed through a filter press for the filtration of oil. By filtration process, it removes moistures dirt from the oil after this process oil is filtered and sent to the storage tanks. By testing samples on some parameters of transformer oil, it will pass for reusing in the transformers.
10
"TRAMSFORMER OIL RECLAMATION'

## Slide 15: PROCESS FLOW CHART OF PLANT
"TRAMSFORMER OIL RECLAMATION'
11

## Slide 16: TRANSFORMER OIL BEFORE AND AFTER RECLAMATION
"TRAMSFORMER OIL RECLAMATION'
12

## Slide 17: PARAMETERS OF TRANSFORMER OIL
"TRAMSFORMER OIL RECLAMATION'
Parameter | Types Of Oils |  |  | 
 | Napthenic Mineral oil (A) | Synthetic Ester oil (B) | Synthetic Ester oil (C) | Silicon Oil (D)
Density (20°C) g/cm³ | 0.89 | 0.97 | 0.99 | 0.96
Viscosity (40°C) mm2/s | 8.9 | 30 | 33 | 35
Breakdown voltage - KV | >70 | >75 | >75 | >50
Max. water solubility (25°C) ppm | 70 | 2500 | 2500 | 200

## Slide 18: CONCLUSION
"TRAMSFORMER OIL RECLAMATION'
we have discussed about the transformer oil, the contaminants present in the transformer oil, why transformer oil needs to be reclaimed and how transformer oil filtration machine reclaimed the transformer oil.

## Slide 19: REFERENCES
"TRAMSFORMER OIL RECLAMATION'
Mansapuram Petrochem Pvt. Ltd.
Google
SSRG-IJEEE

## Slide 20
THANK YOU
"TRAMSFORMER OIL RECLAMATION'
16